## Slide 1: Binary Adder

## Slide 2: Binary Adder
Most Basic arithmetic function is Addition of two binary digits
  0+0=0,
  1+0=1,
  0+1=1,
  1+1=10 (Carry is added to the next higher order pair of significant values)
A combinational circuit that performs addition of two bits is called Half Adder
A combinational circuit that performs addition of three bits is called Full Adder (Adding two half adder)

## Slide 3
Half Adder
Adds two one-bit binary numbers (A and B) and outputs a sum (S) and a carry (C).
X
Y
S
C
0
0
0
0
1
0
1
0
0
1
1
0
1
1
0
1
XOR
AND

## Slide 4
Inputs
Outputs
x
y
z
S
C
0
0
0
0
0
0
0
1
1
0
0
1
0
1
0
0
1
1
0
1
1
0
0
1
0
1
0
1
0
1
1
1
0
0
1
1
1
1
1
1
INPUTS
OUTPUTS
Full Adder
C
Adds three one-bit binary numbers (A, B, C) and outputs two one-bit binary numbers, a sum (S) and a carry (C1).
Notes: K-maps of S shows checkboard configuration. Hence it is X XOR Y XOR Z

## Slide 5
Full Adder

## Slide 6
Full Adder
C = XY + YZ + XZ

## Slide 7
Implementing Full Adder with two half Adders
C = XY + YZ + XZ
= XY + XY’Z + X’YZ
= XY + Z(X + Y)
C

## Slide 8: Binary Subtractor

## Slide 9
Half Subtractor
Subtraction of unsigned binary numbers can be done using complements.
Bo = A’B
D = A XOR B

## Slide 10
Full Subtractor

## Slide 11
Full Subtractor
Like carry in full adder, borrow of full subtractor also takes the form of